## Slide 1
WAN Automation Framework
Infrastructure Resiliency & Deployment Orchestration TechLink Solutions

## Slide 2
Architecture Design
Strategic multi-branch layout connecting Cairo HQ to Alexandria and Giza regional nodes.
•
Dual WAN Ingress: Redundant ISP paths per branch terminating on Core L3.
•
Path Separation: HQ Core isolates transit traffic from campus L2 domains.
•
High Availability: Physical diversity across Gi1/0 to Gi4/0 interfaces.
NETWORK TOPOLOGY OVERVIEW
Logical Segmentation: Strict separation of the management plane (VLAN 10) from end-user traffic (VLAN 20) across all local access ports

## Slide 3
Segment Role | Prefix | Subnet Mask | Design Rationale
WAN Point-to-Point | 192.168.x.x | 255.255.255.252 (/30) | Conserve space, minimize broadcast noise
Inter-Site Transit | 10.10.1.0 | 255.255.255.252 (/30) | L3 Core to Distribution Handoff
Branch LAN (Users) | 10.11.20.0 | 255.255.255.0 (/24) | Scalable local user segmentation
Branch Management | 10.11.10.0 | 255.255.255.0 (/24) | Isolated OOB management access
IP STRATEGIC ADDRESSING

## Slide 4
OSPF Area 0
Single Backbone Area 0 configuration for maximum convergence speed and simplicity.
Self-Healing
Sub-second RIB recalculation upon link state failure ensures zero-touch recovery.
DYNAMIC ROUTING ENGINE

## Slide 5
L2/L3 Access Control
Standardized switching templates across all branches for uniform policy enforcement.
•
VLAN 10: Management SVI for device telemetry.
•
VLAN 20: End-user data segment with DHCP relay to Core.
•
Transit: Routed port FE0/0 isolation on Multi-Layer Switches.
SWITCHING & SEGMENT ARCHITECTURE

## Slide 6
AUTOMATED PROVISIONING
Deployment engine utilizing Python and Netmiko for zero-error baseline configuration.
•
Zero-Touch Provisioning" (Just One Click)
•
Zero Configuration Drift" (Organized)
•
Configuration Deployment Script (initial_deploy.py)
Time/Effort Saved

## Slide 7
Telemetry Logic
Continuous route table polling provides human-readable status dashboards every 30 secs.
LIVE MONITORING TELEMETRY

## Slide 8
Q3 - 2026
Security hardening: Implement IPsec tunnels over OSPF transit links.
Q4 - 2026
SD-WAN Trial: Introduction of centralized policy management.
Q1 - 2027
Cloud Edge: Direct interconnection to Azure/AWS local zones.
Q2 - 2027
AI Ops: Predictive failure analysis via machine learning telemetry.
PHASE 2: STRATEGIC ROADMAP